## Slide 1
CY315 · Wireless and Mobile Security
Defending the Wiretap Channel
A deep-RL approach to artificial-noise power allocation — when Alice's intel on Eve is noisy
Muhammad Ismail · Abubakar Butt · Usman Ali
2023453 · 2023352 · 2023581

## Slide 2
The problem we're solving
Wireless is broadcast. Anything Alice transmits, Eve picks up too.
• Standard fix: artificial noise (AN) sprayed into Bob's null space — Bob hears clean signal, Eve hears signal + jam.
• The knob: how much power to put on the message vs the jamming.
• The classic answer (Goel & Negi, 2008): split it 50/50. Safe but leaves performance on the table.
• The textbook upgrade: optimise the split per channel. Works great — IF Alice has perfect information about Eve. She usually doesn't.
• Plug noisy intel into the textbook optimiser → a confidently-wrong answer that performs WORSE than doing nothing. We'll see this on the next plot.
Slide 2 / 13

## Slide 3
The setting — MISO wiretap channel
Alice (multi-antenna), Bob (legitimate), Eve (eavesdropper)
Alice's intel on Eve is noisy:
κ — CSI quality
κ = 1 → perfect intel κ = 0.4 → realistic (our default) κ = 0 → pure guessing
Green wedge = MRT beam at Bob. Red hatched region = artificial-noise spray.
The dial ρ controls how power is split between green (message) and red (jamming).
Slide 3 / 13

## Slide 4
Two classical answers — and why both fall short
Scheme 1 — Fixed (Goel & Negi, 2008)
Always splits power 50/50. Pros Cannot be misled by bad intel. Always returns a sensible answer. Cons Sub-optimal whenever the channel is asymmetric. Leaves rate on the table at high SNR.
Scheme 2 — Traditional optimiser
Per-channel argmax of Rs against the noisy ĥE. scipy bounded scalar (Brent's method). Pros Provably optimal at κ = 1. Cons Trusts ĥE blindly. At low κ the noise gets amplified, and the optimiser confidently picks the WRONG ρ.
Slide 4 / 13

## Slide 5
BEFORE vs AFTER our AI — same channels, same κ
Left: only existing schemes. Right: with DQN added.
X axis → Transmit power, SNR in dB (0 to 30)
Y axis → Average secrecy rate Rs (bits/s/Hz) — higher is better
Left panel: Traditional (red) drops BELOW Fixed (grey) — trusting noisy intel hurts. Right panel: DQN (green) holds at or above Fixed everywhere.
Slide 5 / 13

## Slide 6
Our approach — train a policy that EXPECTS noisy intel
1. Reframe
Stop trying to find the closed-form optimum each call. Instead, train a policy off-line, across MANY noisy-intel scenarios, that learns when to trust ĥE and when to fall back to safe defaults.
2. Two key inputs
Tell the agent how trustworthy its intel is → feed κ directly into its observation. Tell it the channel geometry → feed the alignment between Bob's beam and the noisy Eve estimate.
3. Single deployable model
ONE trained network handles every (SNR, κ) it sees in the test set. No retuning, no re-optimising at run time. A forward pass replaces an iterative solver.
Slide 6 / 13

## Slide 7
What the agent sees, what it does
State — 7 numbers describing the situation
📡
Bob's channel strength
📡
Eve's (noisy) channel strength
⚡
Transmit SNR
🕒
What it picked last time
📊
How it scored last time
🎯
κ — intel quality
📐
α — beam-vs-Eve alignment
(α formally:)
Action
Pick one of 17 candidate splits between message and AN (steps of 0.05). Discrete → light DQN architecture, fast inference.
Network
Small feed-forward net, 7 inputs → 17 Q-values. Greedy at test time: pick the highest-Q action. Trained with Huber loss + Adam over 7000 episodes.
Slide 7 / 13

## Slide 8
Training — one decision per channel, 7000 channels
Smoothed running-average reward climbs as ε decays to 0.05; policy stabilises in the second half.
7000
training episodes per Nt
≈ 38 s
training cost on a single CPU core
Nt ∈ {2, 4, 8}
three independent models, identical hyperparams
Slide 8 / 13

## Slide 9
Headline result — three schemes, same channels
κ = 0.4, Nt = 4, 400 unseen channels per SNR point
X axis → Transmit SNR (dB)
Top Y → absolute Rs (bits/s/Hz); Bottom Y → gain over Fixed
DQN (green) sits at or above the Fixed baseline (grey) everywhere. Traditional (red, dashed) drops below. Same model, no retuning per SNR.
Slide 9 / 13

## Slide 10
Robustness — the κ sweep and the outage curve
X → CSI quality κ ∈ [0, 1] Y → Rs (bits/s/Hz)
X → target rate R₀ Y → outage P(Rs < R₀)
Drag κ from 1 → 0. Traditional collapses below Fixed near κ ≈ 0.6. DQN never does.
Outage at the same scenario. At R₀ = 4 bits/s/Hz, DQN's outage ≈ 18% vs Traditional's ≈ 26%.
Slide 10 / 13

## Slide 11
Live demo — Streamlit GUI
Switching to the browser — same model, you drag the sliders.
1.
Live test
Pick (Nt, SNR, κ). See three schemes compete side-by-side.
2.
SNR sweep
Hold κ, vary SNR. Watch the curves spread or converge.
3.
κ sweep
Hold SNR, slide κ from 1 → 0. The headline story, live.
4.
Outage
Empirical CDF. How often each scheme misses the target rate.
5.
Geometry
Conceptual sketch — Alice's beam, AN, Bob, Eve.
▶ streamlit run app/streamlit_app.py (default Nt = 8 — where the win is biggest)
Slide 11 / 13

## Slide 12
Takeaways
1. Problem
Plugging noisy intel into the textbook AN-allocation optimiser produces a confidently-wrong split. It actively underperforms the do-nothing baseline once intel quality drops below ~ 0.6.
2. Fix
Train a small DQN over random intel-quality scenarios. Feed the agent its own intel quality and a beam-alignment cue, so it knows when to trust the estimate and when to retreat to a safe default.
3. Outcome
ONE trained policy beats the noisy-CSI optimiser at every Nt and every κ in the test set. Lower outage at the same target rate. ≈ 38 s training cost. Single-pass inference.
Slide 12 / 13

## Slide 13
Thank you — questions?
github.com/MuhammadIsmail009/pls-dqn-miso
Muhammad Ismail · Abubakar Butt · Usman Ali